SJSZ-150/200 PP PE ABS GRANULATION UNIT

I. Extruder

1. SJSZ-150/200 CONICAL SCREW EXTRUDER

This machine is equipped with hard tooth reducer with teeth and axle made of alloy steel and treated by cementite and grinding. The barrel and screw is made of 38CrMoAlA, nitrogenized. Barrel can be cooled by water and fan. Cast aluminum heating ring, JAPAN FUJI frequency conversion, SIEMENS contactor. JAPAN RKC temperature control meter.

Main technical parameters:

A、screw diameter:      Ф150/200mm

B、rotating speed:       120r/min

C、main motor power:    55Kw

D、heating power:       22Kw

E、output:              150-200kg/h

Pelletizing Host

2. SJ-120/8 single screw extruder

This machine is equipped with hard tooth reducer with teeth and axle made of alloy steel and treated by cementite and grinding. The barrel and screw is made of 38CrMoAlA, nitrogenized. Barrel can be cooled by water and fan. Cast aluminum heating ring, JAPAN FUJI frequency conversion, SIEMENS contactor. JAPAN RKC temperature control meter.

Main technical parameters:

    - Screw diameter:       φ120mm

    - L/D:                  8：1

    - Main motor power:    22kw

    - Heating power:       18kw

    - Output:             150-200kg/h

II. Screen changer

This device can prevent the contaminates into the die, improving the quality of finished product . This device is composed of: screen changer; hydraulic pump power: 2.2kw , filter screen size: Φ3-Φ4mm.

Granulating Part

III. Flat Strand die

Made of excellent steel，reasonable flow way，no dead angle

IV. Stainless steel water trough

Made of stainless steel，specification: 650×500mm, length: 4000mm

V. Strand blower

Heating and drying ，heating power: 6kw，blower power: 0.37kw

VI. Pelletizer

Model                               QLJ-3

Motor power                         2.2 kw

Max. capacity                        200 kg/h

Regulation speed type                 inverter

Press type                           pneumatic

Specification of strand cut              φ3×3mm

VII. Blower conveying device

Blower power:                      1.5kw

QUOTATION：USD 42,000 FOB Qingdao Port

Payment: 30% down payment by T/T, balance 70% by T/T or L/C

Delivery time: Within 60 days after receiving prepayment

Guarantee: 12 months from start up

Installation: the seller should notify the buyer to inspect running machine at seller factory after finished and should meet the inspection standard.

Seller sends 2-3 technicians to buyer’ factory for installation and training and buyer will pay for their tickets, accommodation expense, Insurance etc. also buyer pays salary to technicians with USD30 per day